## Slide 1: Circuits Concept Builder

## Slide 2: Overall Vision
PCB board will be powered by a single battery
Size is ~4x8” so that it can be housed inside a off the shelf DIY supply case.
  Case will provide protection against the elements
  Allow for stacking and protect from shorts in the circuit
  PCB can be hot glued to the case
Focus of the circuits will be on fundamental concepts

## Slide 3: Overall Board Layout
3.8”
6.8”
Power supply
“Lucky 7” Circuits
Each circuit will have PADs for multimeter connections

## Slide 4: Overall Board Layout
4”
8”
Power supply
“Lucky 7” Circuits
Each circuit will have PADs for multimeter connections

## Slide 5: Overall Board Layout
4”
8”
In top left of each subset, a switch to turn the circuit on/off

## Slide 6: Power
For now, use a 9V battery
  Need battery holder
Place a master on/off switch right after the 9V battery
Create a battery voltage indicator
  Red, yellow, green
  Use transistors to do this
Use a linear regulator before sending out to the circuit
Have a silk mask showing boundary (probably white)
9V battery holder
Adj Linear regulator
Master on/off switch
Battery voltage indicator
Bank of LEDs showing voltage level
Add a poly fuse

## Slide 7: Power
Use a poly fuse (we will need to do current calcs to size)
Battery circuit monitor (use a comparator)
  Look up curves for Amazon 9V batteries
  Create fixed comparator for 7V. Turn on red LED if lower
Use and ADJUSTABLE linear regulator
  Start with LM317 (add capacitor after to smooth)
  Add square potentiometers with screwdriver faces (CHECK JLCPCB first to see what stock)
Use transistors to create a bank of LEDs.
  As the voltage increases more LEDs turn on
  Underneath each LED have a voltage number silk screened on the PCB
  Have a test point if someone wants to measure directly with a multimeter.

## Slide 8: Test points
In every section of the PCB have test points so that a multimeter can easily probe.
Most have a slight taper at the end
Use a concentric circle design

## Slide 9: General Components
Use Fusion360
  Can do enough SPICE in it
Use 0805 resistors
  Silk screen lots of names
Double sided PCB board
Larger trace size (so students can see it)
Do worst case analysis for poly fuse rating

## Slide 10: Circuit 1 – Through and Across
Learning goal
  Current is through
  Voltage is across
  KVL, KCL, Sum P
PCB notes
  Fixed resistors
  Size R1 to be 2R2 so that the LEDS are different brightness
  ADD MEASURE PADS all throughout
Standard mini SMD slide switch
Test point
560
LED
560
LED
Blue switch shows if power is on
Black lines are masking AND components
Yellow is actual traces (add where needed)
When multimeter is connected to read current through orange pads 2+3 only then the LED will light up.
Dimension of PCB space
1000
2000
CIRCUIT 1
1
2
3
4
POWER

## Slide 11: Circuit 2 – Voltage divider with Loads
Learning Goals
  10% rule
  Voltage divider,
  Sum P, KCL, KVL
  Parallel / series
PCB notes
  Fixed resistors
  Make voltage drops unique across divider
  ADD MEASURE PADS all throughout
Standard mini SMD slide switch
Test point
Dimension of PCB space
560
LED
CIRCUIT 2
1
2
3
4
POWER
1
2
1
2k
3
2k

## Slide 12: Circuit 3 – Mixed DC and Can’t measure resistance in a LIVE circuit
Learning Goals
  Analysis techniques
PCB notes
  Switches on either side of the potentiometer
  ADD MEASURE PADS all throughout
  Current source is this: (make it have the symbol on the silk screen)
https://www.jameco.com/z/LM334Z-LT65-5201--Linear-Technology-IC-LM334Z-LT65-5201-1-to-40V-10mA-Adjustable-Current-Sources-Cut-Tape_23739.html
560
LED
POWER
CIRCUIT 3
1000
1000
1k
LM134
2mA
Standard mini SMD slide switch
Test point
Dimension of PCB space
1
2
3
4
1
2

## Slide 13: Circuit 4 – Series / Parallel with Lights
Learning Goals
  Your model is only an approximation
  Series/parallel
PCB Notes
  Add measure pads
  Add potentiometers
  *** Add a switches to bypass all LEDS with a wire
  Make sure source can disconnect on both sides
switch

## Slide 14: Circuit 5 – RC time constant
Learning goal
  Transient
  555 timer
PCB
  Have switch to turn on/off square wave
  Have potentiometer to set frequency
  Have two R values and a switch to change.
  LED should fade in and out
555 Timer w/ external pot for frequency control
switch

## Slide 15: Circuit 6 – Dependent Voltage Source
Learning Goals
  Dependent source
  Power
PCB Notes
  Use LM358 (or equivalent) single sided op-amp
  Have non-inverting configuration w/ fixed gain of 2
  PADs to measure
Single sided op-amp w/ Gain of 2
Switch (also for op-amp power)
To non-inverting op-amp

## Slide 16: Circuit 7 - Thevenin
Learning Goals
  Thevenin
  Max power transfer
PCB Notes
  Four corner the switches
  PADS
Let .
Four corner the switches!